## Slide 1
SAP APM
Maintenance Flows
Version 1.0
April 2025

## Slide 2: Equipment Criticality Analysis (ECA)
Reliability team members | 
Operation & Maintenance members | 
ECA cross functional team members (Reliability, Operations & Maintenance) | 
Operation & Maintenance Manager | 
Master Data Specialist | 
1.1 Identify systems for ECA
1.4 Collect asset related data such as mining flow diagram, equipment data sheets, SOPs to perform ECA
1.5 Evaluate equipment failure consequences
1.2 Identify assets to perform ECA
1.6 Determine equipment failure frequency
1.8 Approve ECA outcomes
1.7 Determine equipment criticality
s
1.3 Decide ECA cross functional team members
1.9 Populate equipment criticality in ERP
e
Environment Impact
Safety Impact
Financial Impact
Target failure Frequency
Process Flow - ECA

## Slide 3: Failure Mode Effect Analysis
Reliability team members | 
Operation & Maintenance members | 
FMEA cross functional team members (Reliability, Operation & Maintenance) | 
Operation & Maintenance Manager | 
1.1 Identify systems to perform FMEA
1.2 Combine assets to identify asset classes
1.5 Collect data such as process diagram, equipment installation and operation manual to perform FMEA
1.6 Identify potential failure modes
1.3 Identify asset classes with multiple failure modes
1.7 Identify all failure effects
1.8 Identify all failure causes
1.13 Recommend tasks to mitigate failure causes
1.15 Approve FMEA recommendations
1.9 Assess failure mode severity
1.10 Determine failure mode occurrence
1.16 Document FMEA outcomes
1.11 Assign current detection index on each failure mode
1.14 Determine mitigated risk priority number (RPN)
1.12 Determine unmitigated risk priority number (RPN)
s
e
1.4 Decide FMEA cross functional team members
Perform FMEA for asset class with multiple failure modes
For asset classes with single failure mode, initiate maintenance strategy review
Maintenance strategy
Process Flow - FMEA

## Slide 4: Maintenance Strategy
Reliability team members | 
Operation & Maintenance members | 
Cross functional team members (Reliability, Operation & Maintenance) | 
Operation & Maintenance Manager | 
Master data specialist | 
1.11 Implement changes in ERP
1.1 Prioritize assets
1.4 Build failure mode library
RCA recommendation
OEM recommendation
Failure mode effect analysis library
1.9 Create/modify PM tasks lists
1.8 Create operator activity check list
1.6 Determine frequency of maintenance tasks
s
e
1.5 Consolidate and determine maintenance strategies against each failure mode
1.10 Create/modify PM plans
1.7 Approve maintenance strategy
1.2 Decide team members
1.3 Collect data to prepare maintenance strategy
Equipment history
Process Flow – Maintenance Strategy

## Slide 5
1 | Equipment/ Floc extract with make/model details
2 | Existing Maintenance Plans, Task lists, PRTs for class 4 assets
3 | Notification & Work order history for each class 4 assets
4 | Class/Catalogue profile description details
5 | BOM for all class 4 assets
6 | Asset wise FMEA
7 | Failure codes for each asset class
8 | Asset wise production impact/Bad actor analysis data
9 | Asset wise failure impact on HSE
10 | Failure history with damage, cause & catalogue details
11 | Breakdown & Damage Analysis report
12 | MTTR/MTBF Data for each maintainable items
13 | PFDs/PIDs for assets in scope
14 | Maintenance strategies document
15 | List of different condition monitoring tools/ techniques available
16 | O&M Documents/Equipment drawings (GA/Cross-section)
17 | Risk Assessment Matrix
18 | FMEA template & procedure
Data & Documents
Collect Data
(START)
Establish baseline Maintenance strategy
Develop Reliability model
Identify sub classes & major assemblies
Set up FMEA
Template
Identify As-is Counters
Identify Function
Identify Function failure
Identify severity, occurrence & detection
Identify Maintenance task type
Mitigating tasks
Perform FMEA
Perform Reliability modelling
Data collection & Counter identification
FMEA & baseline Maintenance strategy
No. of Asset classes
Sub classes & assemblies
Guidelines for failure mode, effect, cause and recommendation
Maintenance Task for each failure mode
Gather life Data for equipment
Select a lifetime distribution that models life of the item
Estimate the parameters of the distribution
Generate plots estimating reliability or mean life
Replacement interval
1, 4, 13, 16
2, 16
1, 2,4
17,18
5,6,7,8,9,
10,14,15
2,11,14,16
3,5,10,11,12,15,16
Create/ Update replacement strategy
Maintainable Items
Selected Reliability modelling method
Cost analysis
Preventive vs Corrective Maintenance
Update Maint. Plans/Items/task lists/PRTs
(STOP)
Data collection & Counter identification
FMEA & baseline Maintenance strategy
Reliability modelling &
Master Data update
Identify Function failure
Identify failure cause
Identify failure effect
Identify Function failure mode
Replacement Strategy Identification Workflow
1, 4
Counter for each Asset class/assembly
Propose suitable Counters
As-Is counter & strategy
16
Data collection & Counter identification
FMEA & baseline Maintenance strategy
Process Flow – Replacement Strategy

## Slide 6: RCA
Anyone | 
Reliability team members | 
RCA team leader and cross functional team member | 
Operation & Maintenance Manager | 
1.9 Review RCA report & recommendation(s)
1.1 Raise RCA
request
1.2 Approve/Reject RCA request
s
1.3 Decide RCA team leader & members
1.4 Organize & prioritize evidence collection
1.5 Collect data & take interviews
1.6 Develop a timeline
1.7 Perform root cause analysis using a logic tree
1.8 Determine recommendations
1.10 Implement recommendation(s) in ERP
e
Maintenance strategy
Process Flow - RCA

## Slide 7: Reliability Modelling
1. Extract relevant data points to calculate MTBF, MTTR and preventive and reactive maintenance cost for failure of component
3. Identify the components chosen for Scheduled Replacement considering time-based failure and risk potential
5. Create data templates with all the necessary inputs for Reliability modelling to be fed into any Reliability Modelling tool
6. Run the data model on Reliability modelling tool
7. Obtain the optimum replacement frequency
8. Validate the recommended frequency from relevant stakeholders
To be done by Accenture
To be done by Accenture and client
Workshops
Approved
9. Update frequency of scheduled replacement for the component in the m-Item
Yes
No
2. Clean and structure the data to know about material consumption at specific asset location
A
4. Identify the material that is used for these components
A
Process Flow – Reliability Modelling

## Slide 8: Maintenance Journey
Focus on improved master data quality to enable insight generation
Identify all Critical assets & Failure modes to enable predictive maintenance
Update Maintenance Plans/Task list to enable data driven Planning, Scheduling & Execution
Implement predictive maintenance to trigger failure notification
Implement data driven digital use cases to further generate value
Asset Data Management
Asset Hierarchy Build
Bill of Materials
Asset Criticality Assessment
FMEA, Maintenance Strategy
Asset Reliability Management
Maintenance Task list
Maintenance Plan/Item
PRT
Maintenance Optimization & Excellence
Time series Data
Maintenance Data
Analytics based Predictive Asset Management
Predictive Maintenance
Planning & Scheduling optimization
Digital work Execution
Digital Workforce
Digital Asset Management
Remote Operations
Prescriptive Maintenance
Move to digital
Strengthen Fundamentals
Build Standards
Critical Assets & Failure Modes
Location & Materials
Optimum Maintenance Requirement
Planned work visibility
Build Standard & Processes
Asset Data Management
Reliability
Work Management
Maintenance Operating Model
Standards
Assets
Structural Integrity
Asset Integrity
Process Flow – Maintenance Journey

## Slide 9
THANK YOU